Grey Box Fuzzing the IoT
Program Monitoring for Memory
and Power Constraint Embedded Devices
Kevin Läufer <laeufer@berkeley.edu>

---
Problems in Embedded Programming and Testing
- No memory protection:
- all processes can access all memory
- hard to detect and contain failures
- Still predominantly programmed in C
- No logging, no automatic stack traces
- Lacks tools for automated testing

---
Fuzzing Embedded Devices
Fuzzer
Fuzz inputs
USB
???
Execution Control
USB
Execution Trace
???
Image Source: seeedstudio.com
Image Source: STMicroelectronics

---
Fuzzing Embedded Devices

---
Trace Analysis Goals
- Memcheck: V(alid) bits
- find use of uninitialized value
- find double free, use after free
- Dynamic points to analysis:
- detect buffer overflows

---
What’s new?
- Execution Engine based on radare2 intermediate language: ESIL
- Standardized Analysis Tool interface
- Meta data storage

---
Micro Controller Trace Analysis (UCTA)
Custom Analysis Tools
Simulated
Memory
(RAM, Registers)
Program
Facts
(Instructions,
ROM, DWARF)
Execution
Engine

---
ESIL
- Stack based intermediate language
- Emitted by radare2
- radare2 emits wrong code for some ARM instructions
- Makes some analysis steps harder because intermediate values are saved to the stack
- Better separation of concerns

---
ESIL execution

---
ESIL example
strb r4, [r3, 1]
r4,r3,1,+,=[1]
*(char*)(r3 + 1) = r4

---
ESIL bug
strb r4, [r3, 1]!
r4,r3,1,+,=[1],1,r3,+=

---
Analysis Tools Interface

---
Register Taint Analysis

---
Return Address Overwrite Analysis
Exception: Return address overwritten with 0x000000a4 @ pc=0x08000616; originally saved at instr_count=11372 pc=0x080001a0

---
Dynamic Points to Analysis for Arrays on Stack: Idea Sketch
- Use debug information to determine location of arrays on stack frame
- Address always originates from Stack Pointer
- Tag address with array name and bounds once it is derived from the Stack pointer
- Throw exception if address is used to access memory outside array bounds

---
Buggy Function
void buggy_function(const uint8_t* packet) {
char buffer[8];
const uint8_t length = packet[0];
std::memcpy(buffer, packet + 1, length);
}

---
DWARF Debug Information

---
Address Loaded to Stack Pointer
0x080001a8 mov r0, sp
r0 <= ('buffer', 268438432, 268438440)
 @ pc=0x080001a8

---
Address Decrement and Moved to r3
0x0800060a subs r3, r0, 1

---
Load from address and pre increment
0x08000616 strb r4, [r3, 1]!
r3 points to ('buffer', 268438432, 268438440)
 → check if r3 >= 268438432 and r3 < 268438440
   When performing the store

---
Working
- Simulation engine based on ESIL
- Simulation can store meta data
- Flexible and composable analysis passes
- Return address overwrite analysis provides more information

---
Still Missing
- Load DWARF debug information from file
- Interrupt handling
- Implement dynamic points to analysis
- V(alid) bits for memcheck implementation
- Test with larger code base